## Slide 1: Delayed mode quality control of pressure, temperature, and salinity
Jan Even Øie Nilsen
Institute of Marine Research
NorArgo2 Annual meeting, Bergen
December 2nd 2021

## Slide 2: The Matlab toolbox DMQC-fun
Birgit Klein, Ingrid Angel, Kjell Arne Mork, and J. Even Ø. Nilsen
Started in Hamburg 2019
DMQC of core data from Argo floats, incl. salinity calibration
Functions span from download of reference and float data through to a semi automated report and updated D-files
https://github.com/imab4bsh/DMQC-fun.git
New update in progress!

## Slide 3: DMQC-fun at a glance
init_dmqc
init & setup – paths – parameters – list of floats – decisions – all edits in one place – all functions use it
work_log.txt
Explains the whole workflow
A good place to log your overall progress
load_referencedata
ingest for DMQC and OWC
quick-check
update list of reference data
download_floats
from the Coriolis server
NetCDF-files
altimetry comparison
current greylist
prepare_floats
general DMQC
builds the mat-files for OWC
operator_CPcor_new
tool for new Cpcor
near-deployment ship CTD
run_ow_calibration
OWC
all selected floats
write_D
D-files
LaTeX report
reads content saved
by toolbox functions
Coriolis
Coriolis
HD

## Slide 4: init_dmqc
The ‘mother’ script
Table of floats
Operator data (addr. etc.)
Assorted parameters
Paths to directories:
  matlab_ow, float data, reference data, argo toolboxes, my_working_dir
subroutines for initial distribution of necessary files

## Slide 5: 1. load_referencedata
cd ~/Downloads/DMQC
lftp -u <user,password> ftp.ifremer.fr/coriolis/
check for updates
download
run load_referencedata
  Ingests into MATLAB_OWC's climatology
  Map overview of the chosen WMO squares
  Maps and TS, T, and S graphs

## Slide 6: 2. download_floats
Automatic
Based on list and paths in init_dmqc.m

## Slide 7: 3. prepare_floats
Extracts info
Loads data & flags
DMQC of coordinates
Sea Surface Pressure Adjustment (for APEX floats only)
Visual verification of Real-time mode QC flags
Selected automated tests
Visual DMQC of the variables
Correct deep argo/arvor floats pressure dependent conductivity bias
Organise data for OWC

## Slide 8: 4. run_ow_calibration
ow_config.txt and set_calseries.m copied to local folder
edit and re-run
figures put as normal for OWC
parses results and decisions to write_D

## Slide 9: 5. write_D
makes D-files
adds all the flags etc.
checks consistency
SCIENTIFIC_CALIBRATION texts

## Slide 10: 6. Make the report
Follows the flow of the DMQC manual
The master file is fixed
edit notes.tex as you proceed
edit discussion.tex in the end
Input from the matlab functions:
  figures
  snippets of text
  whole tables
  whole sections

## Slide 11: The report
technical info
full overview of flags
plots with flag marks

## Slide 12: The report
Visualisation of spikes etc.
Simple comparison to reference data

## Slide 13: The report
All OWC parameters
All OWC figures
Notes
SCIENTIFIC_CALIB texts
Everything !

## Slide 14: DMQC-fun at a glance
init_dmqc
init & setup – paths – parameters – list of floats – decisions – all edits in one place – all functions use it
work_log.txt
Explains the whole workflow
A good place to log your overall progress
load_referencedata
ingest for DMQC and OWC
quick-check
update list of reference data
download_floats
from the Coriolis server
NetCDF-files
altimetry comparison
current greylist
prepare_floats
general DMQC
builds the mat-files for OWC
operator_CPcor_new
tool for new Cpcor
near-deployment ship CTD
run_ow_calibration
OWC
all selected floats
write_D
D-files
LaTeX report
reads content saved
by toolbox functions
Coriolis
Coriolis
HD